## Slide 1
ABL COAL TRANSSHIPMENT OPERATIONS
Live Tide Data
as a Scheduling Constraint
Using BMKG/BIG tide data to reduce grounding risk
and improve tug-barge flow in Indonesian operations
East Kalimantan / Berau · Indonesia · 2026

## Slide 2
BUSINESS PROBLEM
01
Why Tide
Data Matters
Grounding Risk
Loaded barges reach shallow river sections during low tide and get stuck or grounded.
Lost Sailing Time
Unplanned mooring while waiting for tide to rise creates operational waste.
No System Visibility
Tug masters lack real-time visibility of upcoming tide conditions along the full route.
Blame & Confusion
Field teams, ABL, and planning teams cannot distinguish valid waiting from operational laziness.
"The problem is not asset availability alone — the barge must arrive at each shallow segment at the right tide window."

## Slide 3
02
BMKG TIDE DATA — WHAT IT SHOWS
Source: BMKG Maritime Tide Page · Berau / East Kalimantan Station
Tide Height Forecast — 28 May 2026
03:00 UTC
Highlighted
00:00
04:00
08:00
12:00
16:00
20:00
+2.0m
+1.5m
+1.0m
+0.5m
0.0m
MSL
LAT
DATA POINT — 28 MAY 2026, 03:00 UTC
Station
Berau, East Kalimantan
Date / Time
28-05-2026 03:00 UTC
Timezone
UTC → WITA (+8)
Datum Options
MSL / LAT
MSL Reading
-0.97 m (below MSL)
LAT Reading
+0.80 m (above LAT)
These are the SAME water level
measured against TWO different baselines
WITA (Local) = UTC + 8 hours · Always verify timezone before dispatch

## Slide 4
03
MSL vs LAT
Two baselines,
one water level.
Current Water Level
Mean Sea Level (MSL)
-0.97 m
Lowest Astro. Tide (LAT)
+0.80 m
1.77 m
gap
MSL — Mean Sea Level
Average sea level used as a general reference. A reading of -0.97 m MSL means the water surface is 0.97 m below the average sea level baseline.
LAT — Lowest Astronomical Tide
The lowest predicted tide under average meteorological conditions. A reading of +0.80 m LAT means the water is 0.80 m above this lowest reference.
Why the difference?
At this station, MSL sits ~1.77 m above LAT. Mixing the two datums in navigation calculations produces a 1.77 m error — large enough to cause grounding.
⚠ Navigation clearance must use one consistent datum. Never mix MSL and LAT in the same calculation.

## Slide 5
04
CLEARANCE CALCULATION — CAN THE BARGE PASS?
R I V E R B E D
Water Surface
LOADED BARGE
Draft
3.20 m
Safety
Clearance
0.50 m
Charted
Depth
3.0 m (LAT)
Tide
+0.80m
(LAT)
Formula
Available Depth = Charted Depth (LAT) + Tide Height (LAT)
3.0 m + 0.80 m = 3.80 m
Required Depth
Required = Loaded Draft + Under-Keel Clearance
3.20 m + 0.50 m = 3.70 m
Result
Margin = 3.80 – 3.70 = 0.10 m
Technically passable, but operationally TIGHT
⚠ AMBER — Proceed with caution / Marine approval required
Datum consistency is mandatory: Charted Depth (LAT) + Tide Height (LAT) — never mix with MSL

## Slide 6
05
OPERATIONAL DECISION MATRIX
GREEN
SAFE CLEARANCE
Release / Proceed
Available depth exceeds loaded draft plus safety clearance. Proceed with normal operations.
AMBER
BORDERLINE
Proceed with Marine Approval
Available depth is within acceptable range but margin is tight. Marine officer approval required before release.
RED
INSUFFICIENT CLEARANCE
DO NOT Release
Available depth is below minimum required. Barge must not proceed. Hold at current location until window opens.
WAIT
WAIT RECOMMENDED
Hold & Delay Release
Releasing now results in RED arrival. Waiting ensures the barge reaches the shallow segment during a safe window, improving overall flow.
Key insight: Waiting is sometimes the operationally correct decision — the system must make this explainable and defensible.

## Slide 7
06
SCHEDULING ENGINE LOGIC — MULTI-CONSTRAINT EVALUATION
Trip Proposal
Tug + Barge assigned
ETA Calculation
Departure → Jetty → Shallow Segment
Tide Lookup
BMKG data at ETA timestamp (LAT)
Clearance Check
Available depth vs Draft + Safety margin
Bridge Window Check
Arrival vs permitted bridge crossing time
Joint Decision
GREEN / AMBER / RED / WAIT
ALSO EVALUATED
→ OGV laycan & vessel arrival
→ Jetty & production readiness
→ Coal grade / cargo combination
→ Weather & marine conditions
→ Maintenance / breakdown risk
→ Tug-barge availability
All factors evaluated jointly
before every trip recommendation
Output: Explainable release / hold / wait recommendation with reason and alternative timing

## Slide 8
07
SYSTEM RECOMMENDATION — EXAMPLE SCENARIO
SCENARIO
A loaded barge is ready to depart now.
If released immediately:
→ ETA at Segment B = 03:00 UTC
→ Tide at that time = +0.80 m LAT
→ Required minimum = +1.10 m LAT
→ Clearance shortfall = -0.30 m
→ Grounding risk = HIGH
WITHOUT the system:
Master departs, reaches Segment B at low tide, gets grounded. Waiting cause is unclear. Blame follows.
TRIP STATUS: HOLD
Trip
Tug Barge 12 → Jetty F → OGV MV Berau Star
Loaded Draft
3.20 m / Required depth: 3.70 m
ETA Segment B
28 May 2026 · 03:00 UTC (11:00 WITA)
Tide at ETA
+0.80 m LAT — Below minimum (+1.10 m)
Clearance
3.80 m available vs 3.70 m required → 0.10 m only
Recommended Release: 05:15 UTC / 13:15 WITA
Tide at revised ETA = +1.25 m LAT · Clearance = 0.55 m · Status: GREEN
The 2-hour wait converts a RED grounding risk into a GREEN safe passage.

## Slide 9
08
SYSTEM DATA ARCHITECTURE
BMKG / BIG Tide Data
Official forecast — baseline planning
Tide Adapter
Normalise timezone · datum · format
Normalised Tide Series
station_id · timestamp_utc · datum · tide_height_m
Route Calibration Layer
Map each route segment to relevant station
Safe Movement Windows
GREEN / AMBER / RED per segment per hour
Scheduling Engine
Joint constraint evaluation → release / hold / wait
Dispatcher Dashboard
Explainable recommendations · overrides · audit trail
Observed/local data
corrects forecasts
Route-specific calibration
using AIS/GPS history
Marine override
always possible

## Slide 10
09
IMPLEMENTATION ROADMAP
01
Manual Ingestion
Manual tide upload / BMKG download ingestion. Initial data pipeline setup.
02
Station & Route Mapping
Tide station master. Map each route segment to relevant stations.
03
Window Generation
Daily/intraday tide window calculation with GREEN / AMBER / RED classification.
04
Scheduling Integration
Clearance checks in scheduling engine. Explainable hold / release decisions.
05
AIS / GPS Validation
Compare actual barge position vs predicted. Calibrate forecasts vs actuals.
06
Predictive Calibration
Route-specific calibration using historical grounding/waiting events. ML-ready.
Phase 1 – 3: Foundation · Phase 4: Operational · Phase 5 – 6: Intelligence

## Slide 11
10
KEY TAKEAWAYS
From data to safe passage.
Tide data is a hard scheduling constraint — not background information.
MSL and LAT are different baselines for the same water level. Never mix them.
The right question: will the barge clear the shallow segment at its ETA?
Waiting is often the correct decision. The system makes it explainable and defensible.
ABL starts with BMKG/BIG data, then calibrates using AIS/GPS and historical events.
Goal: reduce grounding risk, reduce waiting waste, improve utilisation without risking OGV commitments.
"The scheduling system should ask not whether a tug and barge are free — but whether the movement will remain feasible across the entire route."